## Slide 1: Meijer-Dematic Discussion
Updated October 13, 2020

## Slide 2: Agenda Topics
Tote Rates
  Inputs / Approach
  Tote Requirements Analysis
    DMS inbound totes
    Empty order store totes
    Completed store totes
    Supply tote returns to DMS
Next steps / discussion
Appendix (from previous meeting)
  Team Intro
    DF86 Berkshire Grey System Overview
  DCD Software needs
    SW Integration Needs
  Timing
  Mechatronics

## Slide 3: Tote Rates Discussion

## Slide 4: Tote flow requirements into and out of Berkshire Grey system
 | Flow | Throughput
A | Empty order totes from dock (Empty order store totes) | 
B | Closed order totes to put walls (Completed store totes) | 
C | Supply totes from sorter (DMS Inbound) | 
D | Used supply totes | 

## Slide 5: Analysis Inputs / Approach Overview
 | Lansing ART System
Station throughput mPacks / hour | 1,150
Station count | 8
Container locations per station / total | 52 / 416
Source Files | cartonized_dlu-2020-02-17.xlsx (+2-26) NOTE: No tote sequence given – Expect reduction in requirements
Days Analyzed | 2/17/2020, 2/26/2020
Total Volume | 243,620 mPacks
OB Totes Generated | 16,843
Average mPacks / tote (supply)* mPacks | 22.45 18.73
Average mPacks / tote (order) mPacks | 22.78 14.46
Data Used
BG Station Information
Assume OB totes processed in the same sequence as today
Set station capacity, process totes in sequence according to capacity
Look at SKU cube, compare to cube of supply tote, apply 85% packing to determine a theoretical packing quantity (covering air and residuals) to determine a mPacks / supply tote by SKU (*weighted by volume above)
Regarding supply tote delivery
  SKU output for first instance of SKU on first order tote
  Later order totes n ‘look back’ at previous output, if previous tote sequence number < n – 416, or if previous supply tote output does not have sufficient calculated quantity, assume a new output required
Analysis Approach
Selected Metrics from Data

## Slide 6: Original Hourly tote and case (mPack) movement for 8/26 – 9/1
Chart: 
8/29/19
8/28/19
8/31/19
Avg. 1,844
9/1/19
1,034
8/26/19
Avg. 9,065
8/30/19
Avg. 398
8/27/19
Supply Totes Hrly
OB Totes Hrly.
Vol. Hrly.
Legend

## Slide 7: Hourly tote and case (mPack) movement for 2/17 and 2/26 8 Stations in Operation
Chart: 
 | 612 | 625 | 598 | 612 | 609 | 605 | 596 | 609 | 595 | 607 | 608 | 617 | 616 | 639 | 630 | 358 | 641 | 642 | 591 | 658 | 694 | 663 | 689 | 713 | 672 | 738 | 606
 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148 | 623.8148
 | 4807 | 3614 | 3684 | 3806 | 3742 | 3826 | 3925 | 3561 | 3888 | 3972 | 3734 | 3783 | 3747 | 3675 | 4063 | 2355 | 4347 | 3958 | 3578 | 3542 | 3447 | 3663 | 3575 | 3635 | 3753 | 3693 | 3197
 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148 | 3724.8148
 | 9205 | 9173 | 9224 | 9199 | 9174 | 9229 | 9192 | 9195 | 9214 | 9192 | 9199 | 9207 | 9180 | 9219 | 9173 | 5581 | 9192 | 9189 | 9215 | 9200 | 9165 | 9220 | 9201 | 9194 | 9208 | 9207 | 8073
 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963 | 9022.963
2/17/20
2/26/20
Legend
Supply Totes Hrly
Vol. Hrly.
OB Totes Hrly.

## Slide 8: Order (ART) totes, throughput requirements
Order totes from dock into Berkshire Grey
Assumed to be same as completion sequence, albeit offset
Significant buffer between dock and tote prep station
Additional buffer after tote prep station and before BG stations
Based on order tote completion sequence, with quantities
  Requirement derived from hourly throughput of system
    1,150 mPacks / hr * 8 cells = 9,200 / hr total
  Order totes processed in sequence, driven by total station capacity
Buffering in and out of BG system
Propose buffering multiple takeaways for surges
Order totes from Berkshire Grey into put walls
Requirement | Order totes / hour
Average | 398 624
Requirement | Order totes / hour
Average | 398 624
Max | 477 738

## Slide 9: Supply (inventory) totes, throughput requirements
Supply totes from sorter into Berkshire Grey
Based on algorithm described on slide 10
  Considers calculated tote quantities, existing outbound tote processing sequence
  Assumes tote rationalization
    Partial totes picked first
  Opportunities likely exist for optimization in Dematic
Supply totes from Berkshire Grey into sorter
On average, supply totes flow back to Dematic at the same total rate as they are fed to BG
Significant buffering via
  Supply tote conveyor to sorter
  DMS infeed lines
  Decant into empty totes, induction
Also looked at totes with contents vs. totes picked clean (again, assuming tote rationalization)
Requirement | Supply totes / hour
Average | 1,844 3,725
Max | 3,222 4,807
Requirement | Supply totes / hour
Average | 1,844 3,725
% totes w/ residual contents (Average totes per hour) | 81.6% 88.0% (1,504) (3,277)

## Slide 10: Tote flow requirements into and out of Berkshire Grey system 8 Stations in Operation
 |  | Throughput | 
 | Flow | Average | Max
A | Empty order totes from dock | 398 | (Buffered)
B | Closed order totes to put walls | 398 | 477
C | Supply totes from sorter | 1,844 | 3,222
D | Used supply totes | 1,844 | (Buffered)
Requirements derived from historical data without actual sequencing / batching, system should be sized appropriately for additional variability and growth, dependent on total DMS capacity
 |  | Throughput | 
 | Flow | Average | Max
A | Empty order totes from dock | 624 | (Buffered)
B | Closed order totes to put walls | 624 | 738
C | Supply totes from sorter | 3,725 | 4,807
D | Used supply totes | 3,725 | (Buffered)
8/26/2019 – 9/19/2019
8 Stations
2/17/2020, 2/26/2020
8 Stations

## Slide 11: Hourly tote and case (mPack) movement for 2/17 and 2/26 6 Stations in Operation
Chart: 
 | 467 | 446 | 468 | 454 | 459 | 448 | 465 | 454 | 452 | 434 | 465 | 449 | 455 | 454 | 463 | 460 | 461 | 478 | 475 | 471 | 358 | 511 | 417 | 470 | 476 | 482 | 527 | 520 | 486 | 521 | 521 | 514 | 518 | 543 | 540 | 261
 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611 | 467.8611
 | 3915 | 2620 | 2839 | 2731 | 2857 | 2846 | 2859 | 2812 | 2962 | 2761 | 2701 | 2950 | 3006 | 2873 | 2742 | 2868 | 2793 | 2956 | 2802 | 2934 | 2355 | 3465 | 2868 | 2778 | 2772 | 2693 | 2485 | 2737 | 2737 | 2590 | 2807 | 2828 | 2738 | 2735 | 2752 | 1403
 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111 | 2793.6111
 | 6903 | 6894 | 6895 | 6910 | 6896 | 6897 | 6906 | 6903 | 6900 | 6899 | 6898 | 6904 | 6888 | 6888 | 6921 | 6901 | 6900 | 6898 | 6895 | 6879 | 5581 | 6881 | 6911 | 6908 | 6896 | 6901 | 6897 | 6880 | 6907 | 6913 | 6897 | 6905 | 6888 | 6909 | 6900 | 3471
 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222 | 6767.2222
2/26/20
2/17/20
Legend
Supply Totes Hrly
Vol. Hrly.
OB Totes Hrly.

## Slide 12: Tote flow requirements into and out of Berkshire Grey system 6 Stations in Operation
 |  | Throughput | 
 | Flow | Average | Max
A | Empty order totes from dock | 398 | (Buffered)
B | Closed order totes to put walls | 398 | 477
C | Supply totes from sorter | 1,844 | 3,222
D | Used supply totes | 1,844 | (Buffered)
Requirements derived from historical data without actual sequencing / batching, system should be sized appropriately for additional variability and growth, dependent on total DMS capacity
 |  | Throughput | 
 | Flow | Average | Max
A | Empty order totes from dock | 468 | (Buffered)
B | Closed order totes to put walls | 468 | 543
C | Supply totes from sorter | 2,794 | 3,915
D | Used supply totes | 2,794 | (Buffered)
8/26/2019 – 9/19/2019
8 Stations
2/17/2020, 2/26/2020
6 Stations

## Slide 13: Appendix

## Slide 14: DF86 System Overview

## Slide 15: System Overview
Dual-Wing Manual Station Overview
DF 86 Deployment
Deployment / System Overview
Project entails 8 Dual-Wing Stations deployed in current tote staging area, with supporting tote conveyor (white conveyor)
Leverages existing ART infrastructure for supply and order totes
Dual-Wing stations serve as put wall replacements
Opportunity to expand and/or add robotic picking the future
Supply Totes
Arrive
Supply Totes
Depart
OB Totes Depart
OB Totes Enter
Tote Workstations
1
2
3
4
3
 | Totes fed to stations via BG conveyor network
 | Operator places mPacks to intermediate conveyors
 | Intermediate conveyors transfer mPacks to shuttles, shuttles deposit to totes
 | Completed store totes ejected and sent to closing stations
 | Supply totes leave station and route to additional stations or return to storage
1
2
3
4
5
5

## Slide 16: SW Integration Needs

## Slide 17: Example Integration
  Ethernet
                Sockets-Based
    TCP
  UDP
  Event-Based
  Kafka
  ZeroMQ
  Request-Response
  JSON RPC
  XML RPC
  Protobuf3 gRPC
  Query API
  REST
  GraphQL
Material / Data Flow
(White / Blue Boxes, respectively)
Protocols currently supported by BG abstraction layer
Example topics to be covered during design phase
  Label Printing
  Exception handling
    No order for tote
    No empty order tote positions available
    Unknown supply tote

## Slide 18
Area | Message | Direction |  |  | Trigger | Purpose | Comment
Admin | Heartbeat | BG | <--> | WCS | Fixed Interval | Used to keep the connection between the RSR and the WCS alive. | 
Admin | Cell Status | BG | ---> | WCS | Status change | Indicates operational status of a specific RSR unit | Information typically used by WCS to understand station availability
Inbound | Supply Tote Notification | BG | <--- | WCS | Tote sent to BG | Notify BG of inbound supply tote | 
Inbound | Store Tote Assignment | BG | <--- | WCS | Order tote assigned for fulfilment | Notify BG of order tote requirements | 
Inbound | Item Information | BG | <--- | WCS | Item data modified | Conveys information about items to be picked by the RSR | Includes robotic picking compatibility Sent per Item, or possibly included in Container assignment (when header processed?)
Outbound | Container Status | BG | ---> | WCS | New container | Updates information about an outbound container | 
Outbound | Order Update | BG | ---> | WCS | Picks / puts | Describes progess in fulfilling requested order | 
Outbound | Store Tote Complete | BG | ---> | WCS | Container completed | Indicates that BG has completed processing the Store Tote | 
Standard RSR Interfaces

## Slide 19: Project Timing

## Slide 20: High-Level Integration / Program Timing
Proposed integration timeline / milestones
Timeline
Key activities
SOW Completion
Integration Design
Onsite Install
Deliverables
High-Level Alignment
Confirm timing
Detailed integration design
Align on dev. / testing methodologies
Development completion
Integration testing completed (offsite)
Berkshire Grey equipment installed
Onsite system integration
Current
Q4 2020
Q1 2021
5/1/2021
Directional approval on approach
Dematic integration scoping
Integration specifications
Integration test plans
Fully-integrated systems
Production Go-Live (6/30/2021)
Current phase
Development / Test
Validated interfaces

## Slide 21: Next Steps
Feedback on analysis, align on requirements
Dematic response to expected flow requirements
Dematic generate ROM for integration

## Slide 22: Appendix System Details

## Slide 23: Proposed System: Semi-Automated Workstation Concept of Operations
Semi-automated store replenishment station concept of operations
Infeed
Homogeneous totes routed via central ticketing to store replenishment station
Completion
Completed totes are kicked to take-away conveyor routed to packing stations
5
1
Singulation
Associate is directed to place single units from donor totes onto one of two cleated conveyors
2
Sortation
Shuttle traverses out and places units into appropriate store container
4
Transfer
Cleated conveyor transfers units into shuttle bucket for sortation
3

## Slide 24: System Layout for 8 Semi-Automated
High-level view of targeted area
Semi-Automated RSR deployment
Objectives
Minimize impact on operations during deployment
Subset of put walls to remain
Maintain operational access
Leverage existing MHE where possible
Single-phased deployment
Berkshire Grey Scope
8 RSR units
All supporting conveyors
Software, IT hardware
Deployment costs
Contingency for unexpected changes
Supply Totes
Arrive
Supply Totes
Depart
OB Totes Depart
OB Totes Enter
Tote Workstations

## Slide 25: Appendix Integration Overview

## Slide 26: Triage / Troubleshooting between Berkshire Grey / Dematic Scope
Physically and logically, there is a relatively clear delineation between Berkshire Grey (BG) and Dematic equipment / scope
In other engagements, BG is responsible for the ‘black box’ containing the sortation equipment, as well as the box and tote conveyor networks therein
BG reports on ‘system availability’ by type to understand accountability and troubleshooting under various scenarios
  When performance falls below expectation, BG will report on any contributing events to this occurrence
  ‘External starvation’ are instances when the BG system cannot perform its functions due to events outside of its control
    OB tote backup (orders unable to close at cells)
    IB tote unavailability (lack of supply totes at cells)
    BG would propose using sensors to detect and report on these occurrences (OB line blocked for X minutes; IB has seen no totes for Y minutes)
  Other events fall within BG scope
    Internal starvation (totes waiting on routing in ‘black box’)
    Intervention required (fault / jam waiting on operator)
Reporting Option 1: Data / Event-Based Reporting
Raw operational data available to Meijer team via network
Accessible through Meijer’s reporting tool of choice
  Note – General applicability for reporting
Could also be reported to existing (Dematic) WCS, or other warehouse monitoring tools
Reporting Option 2: Canned Reporting / Dashboard
Berkshire Grey provisions a BG ‘monitor’ dashboard including these (and other) events, as well as productivity reporting

## Slide 27: Appendix Additional Message Details

## Slide 28
Admin Messages

## Slide 29
Inbound Messages

## Slide 30
Outbound Messages

## Slide 31: Through use of solution proxies, Berkshire Grey systems have great flexibility in protocols and integration schemes
Warehousing Platform(s)
WMS/WCS/WES
Currently Supported Protocols
  Ethernet
                Sockets-Based
    TCP
  UDP
  Event-Based
  Kafka
  ZeroMQ
  Request-Response
  JSON RPC
  XML RPC
  Protobuf3 gRPC
  Query API
  REST
  GraphQL
Berkshire Grey
Solution
Berkshire Grey
Abstraction Layer
  Custom-Created Proxy
  Allows focus on importance of message definitions
  Not limited to integration with Warehouse Platform
    CMMS integration
    Metrics Aggregation / Reporting
Infrastructure
SW Updates
Integration
InfoSec

## Slide 32: User Interfaces
User Interfaces at Workstations
Management User Interfaces
Positioned at individual SASR stations
Requirements / features:
  User login, tracking
  Task direction
  Quality checks
  Error handling
Next Steps
Berkshire Grey will propose user interfaces during detailed design process
Meijer will provide feedback
Interfaces completed prior to installation
Available at workstations and/or on mobile, for general system oversight
Requirements / features:
  Overall system status
  Component (i.e. individual SASR) statuses
  System and component productivities
Strip down to just triage
Jen provide example (?)

## Slide 33: Appendix Timeline Overview